项目名称：高介电常数、低损耗聚合物基导热复合电介质的设计及结构性能调控机理

完成人（限11人）：周文英、党智敏、刘向荣、蔡会武、蔡江涛、左晶等

完成单位（所有单位）：西安科技大学、清华大学、北京化工大学

项目简介：高介电常数（k）、低损耗聚合物电介质因其良好的柔韧、加工性能是制备内嵌式薄膜及高储能密度电容器的理想材料。聚合物电介质在工程应用时因温升导致介质损耗增大，积聚的热量因为聚合物自身的低热导率而无法有效、及时地散失，使得电容器在较低电压下易发生热击穿而遭到破坏。为提高聚合物电介质的击穿电压，本项目通过制备的特殊核壳结构粒子和聚合物复合，设计和制备几类具有3相结构的高热导率的高k-低损耗聚合物复合电介质。通过研究核壳结构壳层厚度变化及控制、填料表面处理、粒径及用量、相对比例、复合工艺等因素对体系的热导率、介电性能的影响，探索提高和改善高k、低损耗聚合物电介质的热导率及热击穿电压的途径及机理，为高导热型、稳定高介电常数-低损耗聚合物电介质的生产提供基础数据和新方法。

主要知识产权目录：

- 文章（限15篇）（文章的第一作者、通讯作者必须为奖励申报完成人）

| 文章题目 | 期刊名称 | 作者（所有人） | 发表时间 | 完成单位（所有） |
| --- | --- | --- | --- | --- |
| Dielectric properties and thermal conductivity of core-shell structured Ni@NiO/poly(vinylidene fluoride) composites | Journal of Alloys and Compounds | Wenying Zhou, Ying Gong, Litao Tu, Li Xu, Wei Zhao, Jiangtao Cai, Yating Zhang, Anning Zhou. | 2017,693 :1-8. | 西安科技大学，哈尔滨理工大学 |
| Towards suppressing loss tangent: Effect of SiO2 coating layer ondielectric properties of core-shell structure flaky Cu reinforced PVDF composites | Journal of Alloys and Compounds, | Wenying Zhou, Li Xu, Liyang Jiang, Jiandong Peng, Ying Gong, Xiangrong Liu, Huiwu Cai, Guangheng Wang, Qingguo Chen. | 2017,710(5):47-56. | 西安科技大学，哈尔滨理工大学 |
| Dielectric spectroscopy characterization of relaxation process in Ni/epoxy composites | Journal of Alloys and Compounds, | Zijun Wang, Wenying Zhou, Lina Dong, Xuezhen Sui, Huiwu Cai, Jing Zhuo, Qingguo Chen. | 2016,682 :738-745. | 西安科技大学，哈尔滨理工大学 |
| Dielectric relaxation dynamics of Al/epoxy micro-composites | Journal of Alloys and Compounds, | Zijun Wang, Wenying Zhou, Lina Dong, Xuezhen Sui, Jing Zhuo, Huiwu Cai, Xiangrong Liu, Qingguo Chen, Jiangtao Cai. | 2016,689 :342-349. | 西安科技大学，哈尔滨理工大学 |
| Dielectric properties and thermal conductivity of PVDF reinforced with three types of Zn particles | Composites Part A: Applied Science and Manufacturig | Wenying Zhou, Zijun Wang, Lina Dong, Xuezhen Sui, Qingguo Chen. | 2015, 79:183- 191. | 西安科技大学，哈尔滨理工大学 |
| Enhanced thermal conductivity and dielectric properties of Al/β-SiCw/PVDF composites | Composites Part A: Applied Science and Manufacturig | Wenying Zhou, Qingguo Chen, Xuezhen Sui, Lina Dong, Zijun Wang, | 2015,71, 184-191. | 西安科技大学，哈尔滨理工大学 |
| Fabrication, thermal, and dielectric properties of self-passivated Al/epoxy nanocomposites | Journal of Materials Science, | Wenying Zhou, Demei Yu. | 2013,48( 22):7960 -7968. | 西安科技大学，西安交通大学 |
| Thermal conductivity and dielectric properties of Al/PVDF composites | Composites Part A: Applied Science and Manufacturig | Wenying Zhou, Jing Zu, Wene Ren | 2012,43 (4):658- 664. | 西安科技大学，西安交通大学 |
| A novel fiber-reinforced polyethylene composite with added silicon nitride particles for enhanced thermal conductivity | Composites Part A: Applied Science and Manufacturig | Wenying Zhou, Caifeng Wang, Tao Ai, Ke Wu, Fenjuan Zhao, Hongzhi Gu. | 2009,40( 6-7):830- 836. | 西安交通大学，中国航天科技集团有限公司，长安大学 |
| Effect of particle size of Al2O3 on the properties of filled thermally conductive silicone rubber | Journal of Applied Polymer Science, | Wenying Zhou, Shuhua Qi, Chunchao Tu, Hongzhen Zhao, Caifeng Wang, Jingli Kou. | 2007, 104(2): 1312- 1318. | 西北工业大学，西安向阳航天材料公司 |
| Study on thermal conductivity of composite BN/HDPE plastics | Thermochimi ca Acta, | Wenying Zhou, Shuhua Qi, Haidong Li, Shiyu Shao. | 2007, 452 (1):36-42. | 西北工业大学，长春工业大学 |
| Thermal conductivity of boron nitride reinforced polyethylene composites | Material Research Bulletin, | Wenying Zhou, Shuhua Qi, Qunli An, Hongzhen Zhao, Nailiang Liu | 2007,42 (10):1863 -1873. | 西北工业大学 |
| Thermally conductive silicone rubber reinforced with boron nitride particles | Polymer composites | Wenying Zhou, Shuhua Qi, Hongzhen Zhao, Nailiang Liu | 2007, 28(1):23~ 28. | 西北工业大学 |
| Surface-Functionalized MWNTs with Emeraldine Base: Preparation and Improving Dielectric Properties of Polymer Nanocomposites | ACS Applied Materials and Interfaces, | Tao Zhou Jun-Wei Zha, Yi Hou, Dong-Run Wang, Jun Zhao, Zhi-Min Dang | 2011, 3 (12), 4557- 4560 | 北京化工大学，北京科技大学 |
| Size-dependent low-frequency dielectric properties in the BaTiO3 /poly(vinylidene fluoride) nanocomposite films | Applied Physics Letters | Ben-Hua Fan, Jun-Wei Zha, Dongrui Wang, Jun Zhao, Zhi-Min Dang | 2012, 100(1): 012903-4 | 北京化工大学，北京科技大学 |

- 专利&软著

| 专利（软著）名称 | 完成人 | 权人 | 专利（软著）号 |
| --- | --- | --- | --- |
| 一种具有低介电常数和低损耗的聚合物电介质及其制备方法 | 周文英 | 西安科技大学 | ZL 2014 1 0206385.7, |
| 一种导热共混聚合物及其制备方法 | 周文英，徐丽 | 西安科技大学 | ZL 2015 1 0763186.0 |
| 一种导热共混聚合物材料及其制备工艺 | 周文英，徐丽 | 西安科技大学 | ZL 2015 1 0763187.5 |
| 一种核壳结构锌粒子/PVDF电介质及其制备方法 | 周文英 | 西安科技大学 | ZL 2014 1 02066590.3, |
| 一种高导热绝缘覆铜板的组方及其制备工艺 | 周文英 | 西安科技大学 | ZL 2013 1 0117820.4. |
| 一种端羟基液体丁苯橡胶改性环氧树脂组方及制备工艺 | 周文英 | 西安科技大学 | ZL 2012 1 0224916.6。 |
| 一种聚合物电介质材料及其制备方法 | 周文英 | 西安科技大学 | ZL 2011 1 0416171.9. |

- 专著等

| 名称 | 作者 | 出版社 | 出版时间 |
| --- | --- | --- | --- |
| 导热高分子材料 | 周文英 | 国防工业出版社 | 2014-4 |